## Slide 1
http://www.dca.iusiani.ulpgc.es/Wind3D
Desarrollo de un método ensemble para la predicción del viento a escala local usando elementos finitos
MINECO
PROGRAMA ESTATAL DE I+D+I ORIENTADA A LOS RETOS DE LA SOCIEDAD
Project: CTM2014-55014-C3-1-R
A. Oliver, E. Rodríguez, R. Montenegro, G. Montero
CMN - 2015
June 29 – July 2, 2015, Lisbon, Portugal

## Slide 2: Contents
Ensemble Wind Forecasting Based on the HARMONIE Model and
Adaptive Finite Elements in Complex Orography
Local scale wind field model
Coupling with HARMONIE meso-scale model
Ensemble method
Numerical experiments
Conclusions
Notes: Decimos que un tetraedro es de Tipo I si está marcado con el indicador de error. Se introducen 6 nuevos nodos en el punto medio de sus aristas y se subdividen cada una de sus cuatro caras en 4 triángulos, uniendo los puntos que se han introducido.
Cuatro subtetraedros quedan determinados a partir de los cuatro vértices del tetraedro original y las nuevas aristas.
Los otros cuatro tetraedros se obtienen al unir los dos vértices opuestos más cercanos del octaedro que resulta en el interior. Estudios de Löhner y Baum aseguran que esta elección produce el menor número de tetraedros distorsionados en la malla refinada. Existen otras dos opciones para subdividir el octaedro, y se podría analizar la calidad de las divisiones, pero aumentaría el coste computacional del algoritmo.
Una vez marcados los tetraedros de Tipo I, para asegurar la conformidad de la malla nos podemos encontrar con tetraedros vecinos que pueden tener 6, 5,..., 1, ó 0 nuevos nodos introducidos.
Aquellos tetraedros que por razones de conformidad tengan marcadas sus 6 aristas pasa automáticamente al conjunto de tetraedros de Tipo I.

## Slide 3
A diagnostic wind model
Governing equations
Let state the least square problem:
: observed wind, which is obtained from horizontal interpolation
and vertical extrapolation of experimental or forecasted data
Objective:
Find the velocity field
that adjusts to
verifying
- Incompressibility condition in the domain
- Non flow-through condition on the terrain

## Slide 4
Mathematical aspects
Mass Consistent Wind Model
where
The solution produces the Euler-Lagrange equations
it yields the governing equations,

## Slide 5
Construction of the observed wind
Mass Consistent Wind Model
Horizontal interpolation

## Slide 6
terrain surface
Construction of the observed wind
Mass Consistent Wind Model
  Vertical extrapolation (log-linear wind profile)
geostrophic wind
mixing layer

## Slide 7
Construction of the observed wind
Mass Consistent Wind Model
● Friction velocity:
● Height of the planetary boundary layer:
the Earth rotation and
is the Coriolis parameter, being
is a parameter depending on the atmospheric stability
is the latitude
● Mixing height:
in neutral and unstable conditions
in stable conditions
● Height of the surface layer:

## Slide 8
Interpolated and resulting wind fields
Mass Consistent Wind Model
Interpolated wind field
Resulting wind field

## Slide 9
HARMONIE model
HARMONIE-FEM Wind Forecast
Non-hydrostatic meteorological model
From large scale to 1km or less scale (under developed)
Different models in different scales
Assimilation data system
Run by AEMET daily
24 hours simulation data
HARMONIE on Canary islands
(http://www.aemet.es/ca/idi/prediccion/prediccion_numerica)

## Slide 10
HARMONIE-FEM wind forecast
Terrain approximation
Topography from Digital Terrain Model
HARMONIE discretization of terrain
Max height 1950m
Max height 925m
Terrain elevation (m)
Notes: Here we can appreciate the big difference between the terrain used by HARMONIE, and the real one

## Slide 11
HARMONIE-FEM wind forecast
Spatial discretization
FEM computational mesh
HARMONIE mesh
Δh ~ 2.5km
Terrain elevation (m)
Notes: There’s also a big difference in the discretization of the problem. In FEM it’s possible to capture the details of the orography

## Slide 12
HARMONIE-FEM wind forecast
Wind magnitude at 10m over terrain
FEM wind
HARMONIE wind
Wind velocity (m/s)
Notes: We can compare the wind velocities obtained at 10m over the terrain with the ones that were given by HARMONIE. We can see that, more or less, the big picture stands, but at the crest line the wind velocity is clearly higher. Max velocity in HARMONIE is 3m/s vs 11.5 in mass consistent

## Slide 13
HARMONIE-FEM wind forecast
HARMONIE data
HARMONIE Grid points with U10 V10 horizontal velocities
Used data (Δh < 100m)
Used data (Δh < 500m)
Notes: In order to compute our wind field we have to use some data from HARMONIE i.e. U10 V10, the Geostrophic velocity, and the Pasquill stability class

## Slide 14
GIS image
Terrain data

## Slide 15
Image segmentation
Terrain data
Roughness length
Obstacles height

## Slide 16
FE solution
is needed
for each individual
Genetic Algorithm
Estimation of Model Parameters

## Slide 17
Ensemble methods
Stations election
Number of genetic experiments |  |  | 
% points | Height tolerances |  | 
 | Infinite | 500 m | 100 m
100 % | 1 | 1 | 1
50 % | 10 | 10 | 10
33 experiments x 24 hours = 792 genetic experiments
Control points
Stations
Δh < 500m
Δh < 100m
Notes: The other 2/3rds are used as known data, and control data for genetic algorithm

## Slide 18
Problem description
Mass Consistent Wind Model
Domain: Gran Canaria Island (60 Km x 60 Km)
Mesh: 84325 nodes, 437261 tetrahedra

## Slide 19
HARMONIE-FEM wind forecast
Location of measurement stations
C635B
C639X
C656V
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 20
Ensemble methods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 21
Ensemble methods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 22
Ensemble methods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 23
Ensemble methods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 24
Ensemble methods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 25
Conclusions and future research
Local Scale wind field model is suitable for complex orographies http://www.dca.iusiani.ulpgc.es/Wind3D
Adaptive meshes improve results from HARMONIE
Local wind field in conjunction with HARMONIE and ensemble method is valid to forecast wind velocities A. Oliver, E. Rodríguez, J. M. Escobar, G. Montero, M. Hortal, J. Calvo, J. M. Cascón, and R. Montenegro. “Wind Forecasting Based on the HARMONIE Model and Adaptive Finite Elements.” Pure Appl. Geophys. (Online). doi:10.1007/s00024-014-0913-9.
Futher research on definition
Study model results under different wind conditions

## Slide 26
Thank you for your attention
Ensemble Wind Forecasting Based on the HARMONIE Model and
Adaptive Finite Elements in Complex Orography
Thanks