## Slide 1
http://www.dca.iusiani.ulpgc.es/proyecto2012-2014
Ensemble Wind Forecasting Based on the HARMONIE Model and
Adaptive Finite Elements in Complex Orography
Albert Oliver (1), Eduardo Rodríguez (1), José María Escobar (1), Gustavo Montero (1), Mariano Hortal (2), Javier Calvo (2), José Manuel Cascón (3), and Rafael Montenegro (1)
University Institute SIANI, University of Las Palmas de Gran Canaria
Agencia Estatal de Meteorología (AEMET)
University of Salamanca

## Slide 2: Contents
Motivation
The Local Scale Wind Field Model
Coupling with HARMONIE
Calibration
Ensemble method
Conclusions
Ensemble Wind Forecasting Based on the HARMONIE Model and
Adaptive Finite Elements in Complex Orography
Notes: Decimos que un tetraedro es de Tipo I si está marcado con el indicador de error. Se introducen 6 nuevos nodos en el punto medio de sus aristas y se subdividen cada una de sus cuatro caras en 4 triángulos, uniendo los puntos que se han introducido.
Cuatro subtetraedros quedan determinados a partir de los cuatro vértices del tetraedro original y las nuevas aristas.
Los otros cuatro tetraedros se obtienen al unir los dos vértices opuestos más cercanos del octaedro que resulta en el interior. Estudios de Löhner y Baum aseguran que esta elección produce el menor número de tetraedros distorsionados en la malla refinada. Existen otras dos opciones para subdividir el octaedro, y se podría analizar la calidad de las divisiones, pero aumentaría el coste computacional del algoritmo.
Una vez marcados los tetraedros de Tipo I, para asegurar la conformidad de la malla nos podemos encontrar con tetraedros vecinos que pueden tener 6, 5,..., 1, ó 0 nuevos nodos introducidos.
Aquellos tetraedros que por razones de conformidad tengan marcadas sus 6 aristas pasa automáticamente al conjunto de tetraedros de Tipo I.

## Slide 3: Motivation
Wind field forecasting for complex terrain
Ensemble methods
Gran Canaria island (Canary Islands)
Notes: Decimos que un tetraedro es de Tipo I si está marcado con el indicador de error. Se introducen 6 nuevos nodos en el punto medio de sus aristas y se subdividen cada una de sus cuatro caras en 4 triángulos, uniendo los puntos que se han introducido.
Cuatro subtetraedros quedan determinados a partir de los cuatro vértices del tetraedro original y las nuevas aristas.
Los otros cuatro tetraedros se obtienen al unir los dos vértices opuestos más cercanos del octaedro que resulta en el interior. Estudios de Löhner y Baum aseguran que esta elección produce el menor número de tetraedros distorsionados en la malla refinada. Existen otras dos opciones para subdividir el octaedro, y se podría analizar la calidad de las divisiones, pero aumentaría el coste computacional del algoritmo.
Una vez marcados los tetraedros de Tipo I, para asegurar la conformidad de la malla nos podemos encontrar con tetraedros vecinos que pueden tener 6, 5,..., 1, ó 0 nuevos nodos introducidos.
Aquellos tetraedros que por razones de conformidad tengan marcadas sus 6 aristas pasa automáticamente al conjunto de tetraedros de Tipo I.

## Slide 4: Motivation
Wind farm energy
Air quality
Notes: Decimos que un tetraedro es de Tipo I si está marcado con el indicador de error. Se introducen 6 nuevos nodos en el punto medio de sus aristas y se subdividen cada una de sus cuatro caras en 4 triángulos, uniendo los puntos que se han introducido.
Cuatro subtetraedros quedan determinados a partir de los cuatro vértices del tetraedro original y las nuevas aristas.
Los otros cuatro tetraedros se obtienen al unir los dos vértices opuestos más cercanos del octaedro que resulta en el interior. Estudios de Löhner y Baum aseguran que esta elección produce el menor número de tetraedros distorsionados en la malla refinada. Existen otras dos opciones para subdividir el octaedro, y se podría analizar la calidad de las divisiones, pero aumentaría el coste computacional del algoritmo.
Una vez marcados los tetraedros de Tipo I, para asegurar la conformidad de la malla nos podemos encontrar con tetraedros vecinos que pueden tener 6, 5,..., 1, ó 0 nuevos nodos introducidos.
Aquellos tetraedros que por razones de conformidad tengan marcadas sus 6 aristas pasa automáticamente al conjunto de tetraedros de Tipo I.

## Slide 5: The Local Scale Wind Field Model

## Slide 6
Problem description
Mass Consistent Wind Model
Experimental data from 4 stations (10 m over terrain)

## Slide 7
terrain surface
Construction of the observed wind
Mass Consistent Wind Model
  Vertical extrapolation (log-linear wind profile)
geostrophic wind
mixing layer

## Slide 8
Construction of the observed wind
Mass Consistent Wind Model
● Friction velocity:
● Height of the planetary boundary layer:
the Earth rotation and
is the Coriolis parameter, being
is a parameter depending on the atmospheric stability
is the latitude
● Mixing height:
in neutral and unstable conditions
in stable conditions
● Height of the surface layer:

## Slide 9
Construction of the observed wind
Mass Consistent Wind Model
Horizontal interpolation

## Slide 10
Mathematical aspects
Mass Consistent Wind Model
Mass-consistent model
Lagrange multiplier

## Slide 11
Construction of the observed wind
Mass Consistent Wind Model
20 m
Interpolated
Resulting

## Slide 12: Coupling with HARMONIE

## Slide 13
HARMONIE model
HARMONIE-FEM Wind Forecast
Non-hydrostatic meteorological model
From large scale to 1km or less scale (under developed)
Different models in different scales
Assimilation data system
Run by AEMET daily
24 hours simulation data
HARMONIE on Canary islands
(http://www.aemet.es/ca/idi/prediccion/prediccion_numerica)

## Slide 14
HARMONIE-FEM wind forecast
Terrain approximation
Topography from Digital Terrain Model
HARMONIE discretization of terrain
Max height 1950m
Max height 925m
Terrain elevation (m)
Notes: Here we can appreciate the big difference between the terrain used by HARMONIE, and the real one

## Slide 15
HARMONIE-FEM wind forecast
Spatial discretization
FEM computational mesh
HARMONIE mesh
Δh ~ 2.5km
Terrain elevation (m)
Notes: There’s also a big difference in the discretization of the problem. In FEM it’s possible to capture the details of the orography

## Slide 16
HARMONIE-FEM wind forecast
Terrain approximation
Notes: Here we can appreciate the big difference between the terrain used by HARMONIE, and the real one

## Slide 17
HARMONIE-FEM wind forecast
HARMONIE data
U10 V10 horizontal velocities
Geostrophic wind = (27.3, -3.9)
Used data (Δh < 100m)
Notes: In order to compute our wind field we have to use some data from HARMONIE i.e. U10 V10, the Geostrophic velocity, and the Pasquill stability class

## Slide 18
HARMONIE-FEM wind forecast
Wind magnitude at 10m over terrain
FEM wind
HARMONIE wind
Wind velocity (m/s)
Notes: We can compare the wind velocities obtained at 10m over the terrain with the ones that were given by HARMONIE. We can see that, more or less, the big picture stands, but at the crest line the wind velocity is clearly higher. Max velocity in HARMONIE is 3m/s vs 11.5 in mass consistent

## Slide 19
HARMONIE wind
HARMONIE-FEM wind forecast
Wind field at 10m over terrain
Wind velocity (m/s)
FEM wind
Notes: Here we can compare the direction of the field. We have to note that HARMONIE doesn’t “see” the island, and the wind field just crosses it. In the FEM solution we can see the way that the island has an effect to the field, while maintaining its S-N principal direction. Although the field in the island looks mess, we zoom it and can see…

## Slide 20
HARMONIE-FEM wind forecast
Zoom
Wind field over terrain (detail of streamlines)
Notes: And, looking at both wind fields overlapped we can see how similar they are.

## Slide 21: Calibration

## Slide 22
FE solution
is needed
for each individual
Genetic Algorithm
Estimation of Model Parameters

## Slide 23
HARMONIE-FEM wind forecast
Stations election
Control points
Stations
Stations and control points
Notes: The other 2/3rds are used as known data, and control data for genetic algorithm

## Slide 24
HARMONIE-FEM wind forecast
Genetic algorithm results
Optimal parameter values
    Alpha = 2.302731
    Epsilon = 0.938761
    Gamma = 0.279533
    Gamma‘ = 0.432957
Notes: We run the genetic algorithm and after 30 iterations with an initial population of 124 individuals, we get the following parameters, with the RMS error seen in plot

## Slide 25
HARMONIE-FEM wind forecast
Forecast wind validation (location of measurement stations)
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 26
HARMONIE-FEM wind forecast
Forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 27
HARMONIE-FEM wind forecast
Forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 28
HARMONIE-FEM wind forecast
Forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 29: Ensemble method

## Slide 30
Ensemble methods
Stations election
Stations (1/3) and control points (1/3)
Control points
Stations
Notes: The other 2/3rds are used as known data, and control data for genetic algorithm

## Slide 31
Ensemble methods
New
Alpha = 2.057920
Epsilon = 0.950898
Gamma = 0.224911
Gamma' = 0.311286
Previous
Alpha = 2.302731
Epsilon = 0.938761
Gamma = 0.279533
Gamma' = 0.432957
Small changes

## Slide 32
Ensemble mthods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 33
Ensemble mthods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 34
Ensemble mthods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 35
Ensemble mthods
Ensemble forecast wind along a day
Notes: Finally with this strategy, we can run all the timesteps given by HARMONIE, and we get the forecasting wind at any point.

## Slide 36: Conclusions

## Slide 37
Conclusions
Local Scale wind field model is suitable for complex orographies http://www.dca.iusiani.ulpgc.es/Wind3D
Local wind field in conjunction with HARMONIE is valid to forecast wind velocities A. Oliver, E. Rodríguez, J. M. Escobar, G. Montero, M. Hortal, J. Calvo, J. M. Cascón, and R. Montenegro. “Wind Forecasting Based on the HARMONIE Model and Adaptive Finite Elements.” Pure Appl. Geophys. (Online). doi:10.1007/s00024-014-0913-9.
The proposed method is a work in progress that looks promising
Ensemble methods provide a promising framework to deal with uncertainties

## Slide 38
Thank you for your attention