## Slide 1: University Institute for Intelligent Systems and Numerical Applications in Engineering
http://www.siani.es/
Congreso de la RSME 2015 – Soluciones Matemáticas e Innovación en la Industria
2-6 febrero 2015, Granada
3-D Wind Field Simulation over Complex Terrain

## Slide 2
Parameterization of the solid surface
Coarse tetrahedral mesh of the meccano
Solid boundary approximation
Inner node relocation
Simultaneous untangling and smoothing
Solid boundary partition
Kossaczky’s refinement
Distance evaluation
Coons patches
SUS
Hexahedron subdivision into six tetrahedra
Meccano construction
Floater’s parameterization
Partition into hexahedra
Algorithm steps
Meccano Method for Complex Solids

## Slide 3
Parameterization
Refinement
Untangling & Smoothing
Simultaneous mesh generation and volumetric parameterization
Meccano Method

## Slide 4
Key of the method: SUS of tetrahedral meshes
Meccano Method
Parameter space (meccano mesh)
Physical space
(optimized mesh)
Physical space
(tangled mesh)
Optimization

## Slide 5
From the i-th solid surface triangulation patch to the i-th meccano face
A’
B’
Physical Space
Parametric Space
C
D
B
A
C’
D’
Q’k
Qk
Q’k =∑j j,k Q’j
Fixed boundary nodes,
Compromise between area and shape
Surface Parameterization of M.S. Floater (CAGD 1997)
Meccano Method

## Slide 6
 Initial cube and its subdivision after three consecutive tetrahedron bisection
6 tetrahedra
12 tetrahedra
24 tetrahedra
48 tetrahedra
Local Refinement: Kossaczky’s Algorithm (JCAM 1994)
Meccano Method
Notes: Decimos que un tetraedro es de Tipo I si está marcado con el indicador de error. Se introducen 6 nuevos nodos en el punto medio de sus aristas y se subdividen cada una de sus cuatro caras en 4 triángulos, uniendo los puntos que se han introducido.
Cuatro subtetraedros quedan determinados a partir de los cuatro vértices del tetraedro original y las nuevas aristas.
Los otros cuatro tetraedros se obtienen al unir los dos vértices opuestos más cercanos del octaedro que resulta en el interior. Estudios de Löhner y Baum aseguran que esta elección produce el menor número de tetraedros distorsionados en la malla refinada. Existen otras dos opciones para subdividir el octaedro, y se podría analizar la calidad de las divisiones, pero aumentaría el coste computacional del algoritmo.
Una vez marcados los tetraedros de Tipo I, para asegurar la conformidad de la malla nos podemos encontrar con tetraedros vecinos que pueden tener 6, 5,..., 1, ó 0 nuevos nodos introducidos.
Aquellos tetraedros que por razones de conformidad tengan marcadas sus 6 aristas pasa automáticamente al conjunto de tetraedros de Tipo I.

## Slide 7
Coons patches
Meccano Method
Coons patches provide a reasonable initial location
in physical domain for inner nodes
  Segment (1D), surface (2D) and cube (3D) interpolations
(a) parametric cube
(b) bilinear interpolation in a rectangle

## Slide 8
Free node
Local optimization
New position for the free node
Objective: Improve the quality of the local mesh by minimizing an objective function
Local mesh
Optimized local mesh
Simultaneous Untangling and Smoothing (CMAME 2003)
Meccano Method

## Slide 9
SUS Code: Weighted Jacobian Matrix on a Plane
x
y
x
y
x
y
Reference triangle
tR
tI
t
Physical triangle
A
W
S = AW -1
: Weighted Jacobian matrix
0
1
2
0
1
2
0
1
2
An algebraic quality metric of t
(mean ratio)
where:
Ideal triangle
tI t
S
Meccano Method

## Slide 10
SUS Code: Local objective function for plane triangulations
Original function:
Modified function:
Modified function (blue) is regular in all R2 and it approximates the same minimum that the original function (red). Moreover, it allows a simultaneous untangling and smoothing of triangular meshes
The extension to tetrahedral meshes is straightforward:
Meccano Method

## Slide 11
Oil field strata meshing
Meccano Method
Boundary surfaces
Volume mesh

## Slide 14: Wind Field Modeling

## Slide 15
Wind Field Modeling Conquered challenges
Use of ensemble methods to obtain local scale wind prediction.
Mass consistent model (MMC) provides a useful method for local scale wind studies.
Local wind 3D field using data measurements.
Automatic process. Few model parameters.
Low computational cost due to use of adaptive tetrahedral meshes and efficient solvers.
Local scale wind field model JWEIA(1998, 2001, 2010)
Integration with mesoscale models PAG (2015)
Coupling with HARMONIE leads to predictive capabilities.
Use of HARMONIE outputs as MMC inputs.
Parameter estimation LNCS(2002), AES(2005)
Ensemble methods PAG (2015)
Use of parallel GAs for parameter estimation.

## Slide 16: Wind Field Modeling Mass Consistent Wind Model
: observed wind, which is obtained with horizontal interpolation and vertical extrapolation of experimental or forecasted data.
Objective: find the velocity field
that it adjusts to
verifying
- Incompressibility condition in the domain:
- Impermeability condition on the terrain:

## Slide 17: Wind Field Modeling Mass Consistent Wind Model
Then,
is the solution of the least-square problem: Find
verifying
where
We can write E as follows

## Slide 18: Wind Field Modeling Mass Consistent Wind Model
Governing equations

## Slide 19: Wind Field Modeling Mass Consistent Wind Model
Construction of the observed wind
Horizontal interpolation

## Slide 20: Wind Field Modeling Mass Consistent Wind Model
terrain surface
  Vertical extrapolation (log-linear wind profile)
geostrophic wind
mixing layer
Construction of the observed wind

## Slide 21: Wind Field Modeling Mass Consistent Wind Model
● Friction velocity:
● Height of the planetary boundary layer:
the Earth rotation and
is the Coriolis parameter, being
is a parameter depending on the atmospheric stability
is the latitude
● Mixing height:
in neutral and unstable conditions
in stable conditions
● Height of the surface layer:

## Slide 22: Wind Field Modeling Estimation of Model Parameters
FE solution
is needed
for each individual
Genetic Algorithm

## Slide 23
Iterative Solution of Sparse Linear Systems
IChol Preconditioner for shifted linear systems
ICholD
ICholN
Cheap strategy: IChol(Aε0)
Expensive strategy: FullIChol

## Slide 24
Iterative Solution of Sparse Linear Systems
IChol Preconditioner for shifted linear systems

## Slide 25: Wind Field Modeling Forecasting over Complex Terrain
Wind3D Code (freely-available)
http://www.dca.iusiani.ulpgc.es/Wind3D/
Notes: Decimos que un tetraedro es de Tipo I si está marcado con el indicador de error. Se introducen 6 nuevos nodos en el punto medio de sus aristas y se subdividen cada una de sus cuatro caras en 4 triángulos, uniendo los puntos que se han introducido.
Cuatro subtetraedros quedan determinados a partir de los cuatro vértices del tetraedro original y las nuevas aristas.
Los otros cuatro tetraedros se obtienen al unir los dos vértices opuestos más cercanos del octaedro que resulta en el interior. Estudios de Löhner y Baum aseguran que esta elección produce el menor número de tetraedros distorsionados en la malla refinada. Existen otras dos opciones para subdividir el octaedro, y se podría analizar la calidad de las divisiones, pero aumentaría el coste computacional del algoritmo.
Una vez marcados los tetraedros de Tipo I, para asegurar la conformidad de la malla nos podemos encontrar con tetraedros vecinos que pueden tener 6, 5,..., 1, ó 0 nuevos nodos introducidos.
Aquellos tetraedros que por razones de conformidad tengan marcadas sus 6 aristas pasa automáticamente al conjunto de tetraedros de Tipo I.

## Slide 26: Wind Field Modeling HARMONIE-FEM wind forecast
Terrain approximation
Topography from Digital Terrain Model
HARMONIE discretization of terrain
Max height 1950m
Max height 925m
Terrain elevation (m)

## Slide 27: Wind Field Modeling HARMONIE-FEM wind forecast
FEM computational mesh
HARMONIE mesh
Δh ~ 2.5km
Terrain elevation (m)
Spatial discretization

## Slide 28: Wind Field Modeling Data interpolation in FE domain: Problems with terrain discretization
Possible solutions for a suitable data interpolation in the FE domain:
Use U10 and V10 supposing it is 10m over the FE terrain (used in this talk)
Given a point of FE domain, find the closest one in HARMONIE domain grid
Other possibilities can be considered
HARMONIE FD domain
FE domain

## Slide 29: Wind Field Modeling HARMONIE-FEM wind forecast
FEM wind
HARMONIE wind
Wind velocity (m/s)
Wind magnitude at 10m over terrain

## Slide 30: Velocity Module - 23/12/2009 - 18:00 h
Wind on the terrain surface
Interpolated field from HARMONIE
Resulting field with the mass consistent model

## Slide 31
Multiple numerical predictions using slightly different conditions
HARMONIE data + MMC model  local wind forecast
The main idea
    Use HARMONIE data as reliable points, as stations or as control points for GAs
    Run different sets of experiments  perturbation
Wind Field Modeling HARMONIE-FEM wind forecast

## Slide 32
HARMONIE U10 V10 data points
U10 V10 horizontal velocities
Geostrophic wind = (27.3, -3.9)
Pasquill stability class: Stable
Wind Field Modeling HARMONIE-FEM wind forecast
Notes: In order to compute our wind field we have to use some data from HARMONIE i.e. U10 V10, the Geostrophic velocity, and the Pasquill stability class

## Slide 33
Used data (2/3 of total)
Wind Field Modeling HARMONIE-FEM wind forecast
Notes: There’s a total of 552 points with u10 and v10 data. We don’t want to use that much, so we discard one third of the data

## Slide 34
Stations (1/3) and control points (1/3)
Control points
Stations
Wind Field Modeling HARMONIE-FEM wind forecast
Selection of Stations

## Slide 35
Ensemble methods
New
Alpha = 2.057920
Epsilon = 0.950898
Gamma = 0.224911
Gamma' = 0.311286
Previous
Alpha = 2.302731
Epsilon = 0.938761
Gamma = 0.279533
Gamma' = 0.432957
Small changes

## Slide 36
Ensemble methods

## Slide 37: Wind Field Modeling Air Quality Modeling
Convection-diffusion-reaction equation
Convective term
Diffusive term
Reactive term
Emissión term
K = diffusion matrix
e = emissión
s(c) = reactive term
Vd = deposition velocity
c = concentration
cemi = stack concentration
cini = initial concentration
u = wind velocity
Boundary
Conditions
Initial Condition
in Ω