## Slide 1
Construction of polynomial spline spaces
over T-meshes for its application in
Isogeometric Analysis
Marina Brovka Doctoral Thesis Defence
Programa de doctorado
Sistemas Inteligentes y Aplicaciones Numéricas en Ingeniería
Instituto Universitario SIANI

## Slide 2
Contents
Introduction and state of the art
Main result of the thesis. Construction of spline spaces
Discussion of the properties of the proposed spaces
Spline parameterization method for 2D geometries
Testing of the proposed strategies. Computational examples
Conclusions and future works

## Slide 3
Introduction and state of the art
Problem statement. Available strategies.
Motivation of our work

## Slide 4: Isogeometric Analysis concept
Isogeometric analysis (Hughes et al, 2005) has arisen as an attempt to unify the Computer Aided Design (CAD) and Finite Element Analysis industries.
The main idea: use for analysis the same functions that are used for CAD representation of the computational domain: B-splines, NURBS, preserving thus the exact geometry
http: // www.3drender. com/

## Slide 5: Isogeometric Analysis vs Finite Element Method
Isogeometric analysis
Variational formulation
Galerkin projection
Isoparametric concept

## Slide 6: Isogeometric Analysis vs Finite Element Method
Basis functions for FEM and IGA:
FEM basis. Lagrange function order 3.
IGA basis. B-splines function order 3.

## Slide 7
IGA: Global parametric mapping
FEM: Local parametric mapping for each element
Isogeometric Analysis vs Finite Element Method

## Slide 8
Isoparametric concept. Basis functions:
Isogeometric Analysis vs Finite Element Method

## Slide 9: Open problems
Parameterization of the domain from its boundary representation.
CAD models provide only the boundary surface of a solid. Application of Isogeometric Analysis requires a full volumetric representation of the geometry.
Local refinement.
Tensor product structure of B-spline spaces does not allow local enrichment of the approximation space. A strategy for construction of spline spaces with local refinement is needed.

## Slide 10: B-splines
Cox- de Boor recursion formula for a set of B-spline functions defined over a knot vector
A set of cubic B-splines inferred from the open knot vector {0, 0, 0, 0, 1/4,1/2, 3/4, 1, 1, 1,1}.

## Slide 11: B-splines
Cubic B-spline function with knot vector
Lagrange basis function of degree 3

## Slide 12
Bivariate B-splines for two global knot vectors:
B-splines

## Slide 13: Local refinement problem for B-splines
A new knot insertion induces the insertion of a knot line extended through the entire domain
global refinement
Superfluous control points!

## Slide 14: T-splines
T-splines ( T. Sederberg et al. 2003)
local refinement
T-junction
T-mesh

## Slide 15: T-splines
Bivariate Cubic T-spline
Inferring local knot vectors for each blending function by traversing T-mesh edges
Local knot vectors associated to anchor tα :
Rational blending functions

## Slide 16
Local details representation, no superfluous control points!
T-splines
Sederberg et al. “T-spline simplification and local refinement”
Watertight merging of patches, no gaps, no overlaps!
Sederberg et al. “Watertight Trimmed NURBS”

## Slide 17
Local refinement
Simplicity of the idea and straightforward implementation (2D and 3D)
Rational blending function: costly derivatives calculus, etc.
No nested spaces
No polynomial reproduction property
Good properties:
Drawbacks:
T-splines for Isogeometric Analysis?
T-splines
No suitable for analysis!

## Slide 18
Poor approximation capacity of T-splines. Improper error convergence
L2 error convergence
T-splines
Adaptive refinement for interpolation problem, using error indicator:

## Slide 19
T-spline parameterization (rational blending functions )
Spline parameterization with the new strategy (polynomial blending functions)
Domain parameterization using rational T-splines
T-splines

## Slide 20
nested spaces
linear independence
optimal locality of the supports
polynomial reproduction property
partition of unity
Complex implementation
Still no examples for 3D
Analysis-suitable T-splines
no analysis-suitable T-mesh
Topological restriction for T-meshes in terms of T-junction intersection
Analysis-suitable T-splines, (M. Scott, 2011)
analysis-suitable T-mesh

## Slide 21: Hierarchical refinement scheme
Hierarchical refinement scheme for IGA
Refinability property of B-splines:
Coarse level functions are replaced by the functions of finer level

## Slide 22
nested spaces
linear independence
polynomial reproduction property
weighted partition of unity
relatively easy implementation
Hierarchical refinement scheme
Excessive extension of the refined area
Not possible to define spline space over a arbitrary mesh
49 new basis functions
Sequential construction of the spaces
Excessive support overlapping:
(Truncated Hierarchical splines)

## Slide 23: Our goal
Multivariate cubic spline spaces with nice properties:
Not too much restrictions over the mesh structure y the refinement pattern
Straightforward implementation both in 2D and 3D
Polynomial reproduction property
Linear independence
Nesting behavior of the spaces
Partition of unity
C2-continuous
Local supports
A practical solution to the problem of local refinement

## Slide 24
Strategy for construction of polynomial spline spaces over hierarchical T-meshes
Mesh pretreatment
Inferring local knot vectors
Modification of local knot vectors

## Slide 25: General scheme
Mesh pretreatment: 0-balancing
Inferring local knot vectors traversing T-mesh edges
Modification of local knot vectors
Three main steps

## Slide 26: Step 1 - Mesh pretreatment
Hierarchical meshes with quadtree/octree subdivision scheme:

## Slide 27
0-balanced quadtree mesh Any node is shared by cells that differ at most in one level of depth
unbalanced mesh
0-balanced mesh
Step 1 - Mesh pretreatment

## Slide 28: Step 2 - Inferring local knot vectors
Inferring local knot vectors
Local knot vectors are inferred by traversing T-mesh edges
Blending functions are associated only to regular nodes of the mesh.
Hanging nodes are skipped while walking across the mesh
T-spline (Sederberg)
our strategy

## Slide 29: Step 3 - Modification of local knot vectors, 2D
Support of the bivariate function Nα with knot vectors:
Frame of the support:
Knot intervals:

## Slide 30
Modification of local knot vectors
Knot vectors of each blending function Nα have to fulfil two conditions:
Condition 2: The frame of the function support should be situated over the mesh skeleton:
Condition 1: Local knot vectors of the d-variate function Nα verify:
Step 3 - Modification of local knot vectors, 2D

## Slide 31
Condition 1:
Condition 2:
two central knot intervals should have the same size, and the other two exterior knot intervals should not be smaller than the central intervals
the four corners of a function support should be situated over the mesh edges
point is not over the mesh edges
point is over the mesh edges
Step 3 - Modification of local knot vectors, 2D
no admissible !

## Slide 32
If any condition is not verified, we modify the local knot vectors by redefining some knots.
Extension rules:
Algorithm
Check Condition 2
Extension rule 2
Check Condition 1
Extension rule 1
Step 3 - Modification of local knot vectors, 2D

## Slide 33
Extension rule 1:
Extension rule 2:
corner is not over mesh edges
corner is over mesh edges
Step 3 - Modification of local knot vectors, 2D

## Slide 34
Extension rule 1
Condition 2 is not satisfied
Condition 1 is not satisfied
Extension rule 2
Step 3 - Modification of local knot vectors, 2D

## Slide 35
Support of the trivariate function Nα with knot vectors:
Frame of the support:
Knot intervals:
12 edges
Step 3 - Modification of local knot vectors, 3D

## Slide 36
Condition 2: Edges of the cuboidal function support should be situated over the mesh faces.
Step 3 - Modification of local knot vectors, 3D

## Slide 37: Some remarks
Support classification
possible knot vector configuration
level of the function support
0
1
2

## Slide 38
Properties of the constructed spline spaces
Non-negative weighted partition of unity
Excessive support overlapping

## Slide 39: Properties of the constructed spline spaces

## Slide 40
Non-negative weighted partition of unity
Properties
partition of unity
New basis :
But some weights can be zero !

## Slide 41
Non-negative weighted partition of unity:
Redundant functions for partition of unity:
Properties

## Slide 42
Possible excessive support overlapping
Additional refinements to avoid support accumulation:
Situation that leads to support accumulation:
Properties

## Slide 43
Parameterization method for 2D geometries from representation of its boundary

## Slide 44: Our result
The proposed method demands a boundary representation of the geometry as input data.
The algorithm obtains, as a result, high quality parametric transformation between 2D objects and the parametric domain.
The key of the method lies in defining an isomorphic transformation between the parametric and physical T-mesh using a new T-mesh untangling and smoothing procedure.
Based on Meccano method
Parameterization method for 2D geometries from its boundary representation

## Slide 45
Good quality parameterization:
Strictly positive Jacobian
Mapping is as conformal as possible
parametric domain
physical domain
Objective

## Slide 46
adapted parametric T-mesh
tangled physical T-mesh
Boundary parameterization and construction of an adapted T-mesh
Objective:
untangle and smooth the T-mesh
General scheme of the method
chord-length parameterization of the boundary
input boundary

## Slide 47
T-mesh optimization
Parametric T-mesh is deformed isomorphically into the physical T-mesh via optimization procedure
optimized physical T-mesh
parametric T-mesh
General scheme of the method

## Slide 48
parametric domain
physical domain
Parametric mapping:
Interpolation:
Construction of a spline representation of the geometry

## Slide 49: T-mesh transformation along the SUS process: Video
optimized physical T-mesh
parametric T-mesh

## Slide 50: Mean Ratio Jacobian of the transformation:
A quality metric of the spline mapping at any point P0

## Slide 51: Mean ratio Jacobian as a quality metric

## Slide 52: Adaptive refinement to improve parameterization quality
Low quality zone is refined and optimized again
inicial T-spline
improved T-spline
Mean ratio Jacobian
Mean ratio Jacobian
Isla de Gran Canaria

## Slide 53: 3D spline parameterization using tetrahedral mesh
tetrahedral parameterization
Spline parameterization
T-mesh vertices are located via tetrahedral parameterization in order to construct spline parameterization
Meccano method

## Slide 54
Testing of the strategy.
Computational examples

## Slide 55: Surface modelling
Floater parameterization
input surface triangulation
parametric domain, triangulation
quadtree T-mesh
spline representation of the surface

## Slide 56: Surface modelling
input surface triangulation
spline representation of the surface

## Slide 57: Interpolation problem
function to approximate:

## Slide 58: Interpolation problem
Adaptive refinement using error indicator based on the exact L2 error:

## Slide 59: Interpolation problem
Error convergence:
adaptive and uniform refinement with our spline functions

## Slide 60: Interpolation problem
Lagrange cubic basis functions
our spline basis functions
Comparison with Lagrange functions:
adaptive refinement for Lagrange basis functions

## Slide 61: Poisson problem in a complex domain
Analytical solution: Steep wave front given by
Residual-type error indicator:

## Slide 62
Domain parameterization. Mean ratio Jacobian as a quality metric
parametric domain
physical domain
Poisson problem in a complex domain

## Slide 63
Final refinement:
parametric domain
physical domain
Poisson problem in a complex domain

## Slide 64
Numerical solution:
parametric domain
physical domain
Poisson problem in a complex domain

## Slide 65
Error convergence:
Poisson problem in a complex domain
adaptive and uniform refinement, IGA

## Slide 66: Poisson problem. Collocation method
- collocation points
Collocation method

## Slide 67
Greville collocation point for the function Ni with local knot vectors
Poisson problem. Collocation method

## Slide 68
Superconvergent collocation points
uniform mesh
T-mesh
Gauss-Legendre quadrarture points:
Poisson problem. Collocation method

## Slide 69
Error convergence
Poisson problem. Collocation method

## Slide 70: Eigenvalue problem
Generalized algebraic eigenvalue problem:
Exact solution:

## Slide 71
Comparison of the exact eigenvalues and numerical eigenvalues obtained with IGA and FEA.
spectrum
relative error of spectrum
Eigenvalue problem

## Slide 72
Adaptive refinement to approximate the 11-th eigenpair:
Eigenvalue problem

## Slide 73
Residual-type error indicator:
Eigenvalue problem

## Slide 74
Error convergence:
Eigenvalue problem

## Slide 75: Kellogg function
Discontinuous diffusion coefficient:
Solution:

## Slide 76
Adaptive refinement for FEM and IGA with C0 –splines along the axes:
Kellogg function
Error estimator:
Final mesh, IGA
Final mesh, FEM

## Slide 77
Strategy with additioanal refinements to avoid excessive support accumulation:
normal adaptive refinement
adaptive process with additioanal refinements
Kellogg function

## Slide 78: 3D Poisson problem
Analytical solution:
oscillation parameter
spline approximation of sphere portion domain

## Slide 79
Final mesh of adaptive refinement:
parametric domain
physical domain
3D Poisson problem

## Slide 80
Numerical solution:
parametric domain
physical domain
3D Poisson problem

## Slide 81
Error convergence:
3D Poisson problem
adaptive and uniform refinement, IGA

## Slide 82: 3D Helmholtz equation with variable frequency
Solution:

## Slide 83
initial mesh, IGA
final mesh, IGA
initial mesh, FEM
final mesh, FEM
Adaptive refinement:
3D Helmholtz equation with variable frequency

## Slide 84
Error convergence:
3D Helmholtz equation with variable frequency
adaptive refinement for IGA and FEM

## Slide 85
Summary, conclusions and future works

## Slide 86
For a given strongly balanced T-mesh, it allows to obtain a set of cubic spline functions that span a space with nice properties: C2-continuous, polynomial reproduction property, nested spaces, linear independence.
Simple rules for inferring local knot vectors to define spline blending functions
Straightforward implementation in 2D and 3D
We have developed a new strategy for constructing cubic spline spaces over quadtree(2D) and octree(3D) T-meshes
Our result

## Slide 87: Future works
Proof of the properties of the spline spaces is needed: nesting behaviour of the spaces for 3D case and linear independence for 2D and 3D cases;
Extend the method for: .
repeated interior knots
spline spaces over complex, polygon type, parametric domains
Some improvements of the strategy can be done:
excessive support overlapping can take place during the adaptive refinement;
strictly positive partition of unity is desirable
More sophisticated rules are needed!

## Slide 88
Gracias !