## Slide 1
http://www.dca.iusiani.ulpgc.es/proyecto2012-2014
Tetrahedral Mesh Optimization Combining Boundary and
Inner Node Relocation and Adaptive Local Refinement
Socorro G.V.(1), Ruiz-Gironés E.(2), Oliver A.(1), Cascón J.M.(3), Escobar J.M.(1), Sarrate J.(2) and Montenegro R.(1)
(1) University Institute SIANI, University of Las Palmas de Gran Canaria, Spain
(2) Laboratori de Càlcul Numèric (LaCàN), Universitat Politècnica de Catalunya – BarcelonaTech, Spain
(3) Department of Economics and Economic History, University of Salamanca, Spain

## Slide 2
Motivation
Mesh Genus-Zero Solids
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 2
Mesh genus-zero solids and get a valid volumetric parameterization
Improve the quality of meshes generated ussing the Meccano method
Main drawback: boundary nodes attached at their location
  Smooth of bondary nodes
(a) boundary surfaces
(b) parametric domain

## Slide 3
The Meccano Method
Surface Parameterization
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 3
Map physical boundary surface to meccano boundary
(a) solid boundary surfaces
(b) parametric domain

## Slide 4
The Meccano Method
Surface Capture
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 4
Mesh and refine the meccano to capture solid surfaces
(a) refined meccano mesh
(b) solid mesh

## Slide 5
The Meccano Method
Inner Nodes Location
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 5
Apply Coons patches to get a reasonable location for inner nodes
(a) solid mesh before Coons patches
(b) solid mesh after Coons patches

## Slide 6
The Meccano Method
Untangle and Smoothing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 6
Simultaneous untangle and smoothing to get a valid mesh
(a) tangled solid mesh
(b) untangled and smoothed solid mesh

## Slide 7
The Meccano Method
Resulting Volume Parameterization
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 7
Volumetric parameterization from uniform structure Kossascky mesh to solid in physical domain
(a) uniform Kossascky meccano mesh
(b) solid mesh in physical domain

## Slide 8
Tetrahedral Mesh Smoothing
Inner Node Smoothing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 8
Unconstrained optimization problem in 3D physical domain
  Physical coordinates as optimization variables
  Quality measurement in physical domain
Parametric counterpart as ideal reduce the distortion
(a) before optimization
(b) after optimization

## Slide 9
Tetrahedral Mesh Smoothing
Boundary Node Smoothing. Parameterizations
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 9
Exploit mesh parametrization to simplify the optimization problem
3D (physical)
surface constrained
2D (parametric)
rectangle constrained
mesh parameterization
(a) parametric domain
(b) physical domain

## Slide 10
Tetrahedral Mesh Smoothing
Boundary Node Smoothing. Optimization
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 10
Optimization
  Parametric coordinates as optimization variables
  Quality measurement in physical domain
(a) Initial locations
(b) locations after smoothing

## Slide 11
Tetrahedral Mesh Smoothing
Boundary Node Smoothing. Parametric Domains
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 11
Creating an additional parametric domain for smoothing porpouse only
parametric domain R
(regular Kossascky mesh)
parametric domain S
(no regular Kossascky mesh)
physical domain
volumetric
parameterization
Floater’s
parameterization

## Slide 12
Tetrahedral Mesh Smoothing
Validity of Boundary Mesh
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 12
Geometry preservation
The resulting mesh is tangled. There are no inverted tetrahedral but some of them are overlapped no valid mesh
(a) parametric domain
(b) physical domain

## Slide 13
Tetrahedral Mesh Smoothing
Boundary Node Smoothing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 13
Imposing validity for boundary faces of the meccano
over star area
  Extra term in the objective function
  that penalties tetrahedral collapse in
  the parametric domain.

## Slide 14
Tetrahedral Mesh Smoothing
Boundary Node Smoothing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 14
Analogous procedure for edge (1D) optimization
Boundary nodes smoothing could cause loose of both volume and geometry
  Iterative Refinement, untangle and smoothing stages

## Slide 15
Tetrahedral Mesh Smoothing
Bound Smoothing Area (Buffering algorithm)
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 15
Mesh must be smoothed after refinement
Buffering algorithm focus smoothing in areas where refinement toke place
  Initialize with new nodes a buffer of pending nodes to smooth
  Smooth first pending node
  If displacement ≥ prescribed threshold enqueue neighbor nodes
  If any pending node return to 2
  Drastic reduction in the number of star to smooth

## Slide 16
Aplications
Oil Field Meshing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 16

## Slide 17
Aplications
Oil Field Meshing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 17
Initial coarse mesh

## Slide 18
Aplications
Oil Field Meshing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 18
Coons patches

## Slide 19
Aplications
Oil Field Meshing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 19
Inner nodes smoothing

## Slide 20
Aplications
Oil Field Meshing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 20
Boundary nodes smoothing

## Slide 21
Aplications
Oil Field Meshing
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 21
Tetrahedral quality
Nbr. of nodes 8213
Nbr of cells 33104 Min quality 0.0043 Mean quality 0.649 Max quality 0.986

## Slide 22
Aplications
Troposphere Meshing for Wind Forecast
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 22
Notes: Brief presentation.

## Slide 23
Conclusions
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 23
Conclusions
  An innovative method has been developed for both, boundary smoothing and volumetric parametrization of genus-zero solid
  This work upgrades The Meccano Method by adding boundary nodes relocation
  The procedure obtains good quality meshes
  The idea can be applied to any mesh generation method that uses surface parameterization
  The procedure requires minimum user intervention
  The algorithm has a low computational cost and admits paralellization

## Slide 24
11th World Congress on Computational Mechanics (WCCM XI). 20 – 26 July 2014.
Tetrahedral Mesh Optimization Combining Boundary and Inner Node Relocation and Adaptive Local Refinement - 24
  Thanks for your attention!
Questions?