## Slide 1: Simulating large emitters using CMAQ and a local scale finite element method. Analysis in the surroundings of Barcelona

## Slide 2: Motivation
To Improve the prediction at fine scales:
  Large emitters
  Near source transport and chemistry
Current approaches:
  Nested grid modelling
  Adaptive grid modelling
  Hybrid modelling
  Plume-in-grid modelling
  Statistical models
  CFD

## Slide 3: Proposed approach
In this work we propose to compare two different approaches
  WRF-ARW/AEMM/CMAQ
    Nested grid modelling
    1km – 300m
  Adaptive Finite Element method
    Plume-in-grid modelling

## Slide 4: Proposed approach
WRF-ARW/AEMM/CMAQ
Meteorology
Emissions
Transport and reaction
Mass consistent model (Wind)
Local FEM
Transport reaction
Plume rise (Briggs)
Initial and Boundary
conditions

## Slide 5: Outline
WRF-ARW/AEMM/CMAQ model
Local scale Finite Element model
Application to Barcelona surroundings
Conclusions

## Slide 6: WRF-ARW
The mesoscale meteorological model used is Weather Research and Forecasting—Advanced Research (WRF-ARW) version 3.6.1
Specially suited to the subscale grid modelling
Time-splitting methods, and high order (both time and space)

## Slide 7: AEMM
Air Emission Model of Meteosim (AEMM v3.0) developed by Meteosim S.L.
Numerical, deterministic, Eulerian, local-scale model
It allows to obtain the intensity of emissions in different areas, either anthropogenic (traffic, industry, residential, etc.) or natural (emissions caused by vegetation or erosion dust) for the area of interest

## Slide 8: CMAQ
CMAQ v5.0.1
CB-5 chemical mechanism
AERO5 aerosol module
EBI solver
Discretization 1km
The WRF-ARW/AEMM/CMAQ approach has been used successfully in urban areas (Catalonia, Madrid), industrial areas (Tarragona, Ponferrada), and arid areas (Perú, Chile)

## Slide 9: Adaptive Finite Element Method
Convection-Diffusion-Reaction equation
Wind field
Plume rise
FEM discretization
Adaptivity

## Slide 10: Adaptive finite element method
Convection – diffusion – reaction equation
A. Oliver et al. Adaptive Finite Element Simulation of Stack Pollutant Emissions over Complex Terrains. Energy 2013.

## Slide 11: Wind field
Interpolate Wind field from WRF-ARW
Mass-consistent model

## Slide 12: Plume rise
Briggs equations
    Buoyancy Momentum

## Slide 13: FEM discretization
  Temporal discretization: Crank-Nicolson
  Spatial discretization: Least Squares FEM
  System solver: Conjugate gradient preconditioned with an Incomplete Cholesky Factorization

## Slide 14: Adaptivity
Mesh adaptation
  Mesh is only adapted to topography and plume rise
  Necessity to adapt to the solution
  Error indicator using log (wide range of solutions)
Mesh refinement fixing a minimum size
L. Monforte and A. Pérez-Foguet. A multimesh adaptive scheme for air quality modeling with the finite element method. Int. J. Numer. Meth. Fluids 2014

## Slide 15: Application
Barcelona surroundings

## Slide 16: Results
Barcelona surroundings
CMAQ nested domains

## Slide 17: Results
Zoom of the nested domain

## Slide 18: Results
Day: 2/12/2013
  High concentration levels
Simulation 48h (24h spin up)
CMAQ grid resolution 1km, 32 layers
FEM domain 20x20km, resolution from 1km to ~1m

## Slide 19: FEM Mesh

## Slide 20: FEM Mesh

## Slide 21: Max. 1h levels
FEM CMAQ

## Slide 22: Measurement stations

## Slide 23: Near emitter station

## Slide 24: Near emitter station
Streamlines from the emitter

## Slide 25: Near emitter station
Hour description of wind not enough
Streamlines from the emitter

## Slide 26: Near emitter station

## Slide 27: Station distant to the emitter

## Slide 28: Station distant to the emitter

## Slide 29: Conclusions
Combination of a nested grid and a local scale finite element model is a promising approach
The WRF-ARW/AEMM/CMAQ system using a 1km grid captures the observed data far from the emitter
Near the emitter, the finite element model is closer to the measured data, while far from the emitter the CMAQ-ARW model is better.

## Slide 30: Future work
Use an smaller resolution for the wind field in the local scale model.
Explore how to combine both models, operationally, in a hybrid model.